## Slide 1: Optimisation for CPU Inference (Chapter 4)

## Slide 2: Learning Objectives
  Early AI (1950s-1990s) – Symbolic AI & Classical Machine Learning
    Perceptron (1958) – Frank Rosenblatt’s simple neural network, later shown to be limited.
    Backpropagation (1986) – Key breakthrough by Rumelhart, Hinton, and Williams.
    Support Vector Machines (1990s) – Rise of kernel methods for classification.
Krizhevsky, Alex, Ilya Sutskever, and Geoffrey E. Hinton. "Imagenet classification with deep convolutional neural networks." Advances in neural information processing systems 25 (2012).

## Slide 3: Quantization Methods on ARM
Linear Quantization maps floating point range to quantized range with an optional offset
Quantization
Dequantization:
Floating Point Range
Floating-point
Integer

## Slide 4: Data Formats on ARM
  Data Formats (fp32 -> fp16/bfp16 -> int8 -> int4)
    Reduces bit width of parameters to lower memory and compute cost.
    Reducing Bit-widths reduces numerical precision (the number of representable values)
    Bf16 has higher dynamic range compared to fp16
int4
int8
fp16
fp32
  Sign bits
  Exponent bits
  Mantissa bits
  Value bits
bf16

## Slide 5: Pruning Techniques on ARM
Learning Both Weights and Connections for Efficient Neural Network [Hanetal., NeurIPS 2015]
Pruning removes redundant weights, neurons or activations from the network.
High level of unstructured sparsity can be achieved with minimal accuracy loss
A common approach, Iterative Magnitude Pruning:
Dense Network
Pruned Network
Neuron Pruning
Connection Pruning
Train a Dense Network
Remove smallest p% of weights
Fine-tune
Output Pruned Network

## Slide 6: Overview of ARM’s SIMD Capabilities
Single instruction multiple data (SIMD)
  Performs the same operation on multiple data elements concurrently
  Increases throughput for matrix multiplication
  Arms advanced implementation of SIMD instructions is the NEON feature.
Arm Advanced SIMD Features:
  Scalable Vector Extension
    Increased vectorization and enhanced throughput.
    Introduces vector-length agnostic approach.
  I8MM
    Feature of Arm Processors to accelerate integer matrix multiply
    Specifically suited for INT8 quantized networks
    Multiplies 2x8, 8x2 matrix segments to output 2x2 results.
  SME
    Builds on NEON to use 2D vectorization
    Specifically developed for matrix multiply operations
    extends SVE concepts by adding dedicated instructions for matrix-based computations.
  NEON Vector Multiplication

## Slide 7: I8MM: Accelerated Int8 Matrix Multiplication
Quantization can reduce precision to INT8
I8MM designed to specifically accelerate INT8 Matrix Multiplication.
  SMMLA (vector) instruction will deliver a peak integer multiply throughput that is at least as high as can be achieved using two SDOT (vector) instructions
  Mandatory features of Armv8.6+
SMMLA <Vd>.4S, <Vn>.16B, <Vm>.16B
  <Vd> the destination register
  <Vn> is the first source register
  <Vm> the second source register

## Slide 8: Scalable Vector Extension (SVE)
No fixed width (unlike NEON) – the same code can scale from 128 to 2048 bits.
Vector length must be a power of two (
Guarantees, same implementation can run on different widths of SVE
SVE Registers (Z0-Z31) shared with NEON (last 128 bits)
Predicate Registers (P0-P7) Provide fine-grained control over which elements in the vector are active.
SVE Registers (Z0-Z31)
Predicate Registers (P0-P7)

## Slide 9: Scalable Matrix Extension (SME)
An extension to SVE to operate on matrix tiles
Streaming SVE mode adds new instructions specifically for matrix multiplication
Dedicated matrix tile storage (ZA) array
  Just like SVE, SME has variable length tile vector storage (SVL)
Matrix tile storage (ZA Array)
Dedicated matrix tile storage (ZA) array
  As SVE had an variable length vector (SVL)
  SME has variable length tile vector storage (SVL)
SME New instructions
  Outer Product () operations.
  Load/Store and Transposition
  Additional Arithmetic and Logical Operations (e.g. zeroing tiles)
ZA Array memory access
  ZAOH.B[n] accesses the nth row
  ZAOV.B[n] accesses the nth column

## Slide 10: Loop Re-ordering
Naïve matrix multiplication loops can be re-ordered.
  The ordering affects memory access pattern.
  Loop re-ordering improves access pattern in A and B
Naïve Matrix Multiplication
Row Access = A[6:12]
Column Access = A[0], A[7], A[13], …
When Matrices are stored in Row-Major order
Loop Re-ordered Matrix Multiplication

## Slide 11: Tiling
Matrix Multiplication is an Extremely parallelizable operation.
Matrices of GenAI models are huge!
  Can be N >> 1024
Main memory access slow, cache is fast.
  Global DRAM is much slower than on-chip caches
Reducing global memory access, speeds up inference.
  Tiling reuses rows/columns in cache, boosting performance
  Increases Ops/DRAM memory access ratio.
Naïve matrix multiplication
Tiled matrix multiplication

## Slide 12: Loop Unrolling
Matrix Multiplications provide branching overhead
  Have to evaluate:
    I < N
    J < N
    K < N
Reduces branching overhead
Better Instruction scheduling
  Exposing more independent operations, allows CPU to schedule parallel pipelines.
Reduced Branch Misprediction Penalties
Naïve matrix multiplication
Naïve matrix multiplication

## Slide 13: Multi-Core Parallel Programming on ARM
Matrix multiplication is highly parallelizable.
  It can exploit multiple cores or threads simultaneously for faster execution.
Multi-threading boosts throughput.
  Different parts of the matrix multiplication can run on separate threads or cores.
Modern Arm and cloud processors often support simultaneous multithreading (SMT).
  This allows more than one thread of execution per core, further increasing parallelism.
Parallelized Naïve Matrix Multiplication

## Slide 14: ARM-Optimised uKernel & Runtime Libraries
  Early AI (1950s-1990s) – Symbolic AI & Classical Machine Learning
    Perceptron (1958) – Frank Rosenblatt’s simple neural network, later shown to be limited.
    Backpropagation (1986) – Key breakthrough by Rumelhart, Hinton, and Williams.
    Support Vector Machines (1990s) – Rise of kernel methods for classification.
Krizhevsky, Alex, Ilya Sutskever, and Geoffrey E. Hinton. "Imagenet classification with deep convolutional neural networks." Advances in neural information processing systems 25 (2012).

## Slide 15: Real-World Integration on ARM

## Slide 16: Summary
  Early AI (1950s-1990s) – Symbolic AI & Classical Machine Learning
    Perceptron (1958) – Frank Rosenblatt’s simple neural network, later shown to be limited.
    Backpropagation (1986) – Key breakthrough by Rumelhart, Hinton, and Williams.
    Support Vector Machines (1990s) – Rise of kernel methods for classification.
Krizhevsky, Alex, Ilya Sutskever, and Geoffrey E. Hinton. "Imagenet classification with deep convolutional neural networks." Advances in neural information processing systems 25 (2012).

## Slide 17: Questions and Discussion